## Slide 1: Digital Logic SNN on FPGA hardware
Bhaskar Vyas - 181EC109
Mohammed Ibrahim Ali - 181EC225

## Slide 2: Problem Statement Reproduce the work done in the research paper by Xiping Ju and Biao Fang, et al. Use CNN to ‘train’ the SNN Implement the SNN on Intel Cyclone V FPGA Analyse the performance and efficiency results of the network

## Slide 3: Spiking NN? Mimics biological neurons When state exceeds membrane potential, a spike is sent Neuron state decays over time due to leakage
Notes: Challenges:
Implementation of SNN in digital logic
Training snn; converting mnist image to spike trains

## Slide 4: Research Objectives Stage 1 Stage 2 Stage 3 Stage 4
Literature review
Theoretical analysis of SNN training process
Build, train CNN
Design and model SNN
Verilog design, including testing module
Implementation on FPGA
Performance analysis
Testing with HPC/automation

## Slide 5: Design Methodology
7 layer CNN model
ReLU as activation function
Max Pooling operation used
Trained on MNIST dataset

## Slide 6: Spike train encoder
conversion of information to artificial neuron spikes
rate coding is implemented.
information is carried by the firing rate of the neuron.
Fixed uniform spike trains generation algorithm
Pixel values are normalized between 0 and 1 as firing rate
Compute total spikes fired based on length of time window and firing rate
Spikes uniformly distributed along time window
Notes: Explain the process with example:
Length of time 1 sec; 5ms steps -> total spikes = 1/0.005 = 200
Pixel value 32 -> normalized to ~0.125; 200 * 0.125 = 140 spikes;
one spike every 1/0.125 = 8 time steps = 40ms

## Slide 7: Spike Neuron
Implemented in Verilog
Uses Discrete integral steps based on positive clock edge
No decay

## Slide 8: Results

## Slide 9: Future Plan Performance and efficiency analysis on FPGA Use HPC to simplify testing on FPGA Run NN on GPU using MATLAB

## Slide 10
Questions?

## Slide 11: References
https://direct.mit.edu/neco/article-abstract/32/1/182/95561/An -FPGA-Implementation-of-Deep-Spiking-Neural?redirectedFrom=fulltext
A Cost-Efficient High-Speed VLSI Architecture for Spiking Convolutional Neural Network Inference Using Time-Step Binary Spike Maps